## Slide 1: 9.1 Introduction
We have so far studied only the simplest models of computer systems; classical single-processor von Neumann systems.
These slides present a number of different approaches to computer organization and architecture.
Some of these approaches are in place in today’s commercial systems. Others may form the basis for the computers of tomorrow.
Notes: 1

## Slide 2: 9.4 Parallel and Multiprocessor Architectures (1 of 21)
Parallel processing is capable of economically increasing system throughput while providing better fault tolerance.
The limiting factor is that no matter how well an algorithm is parallelized, there is always some portion that must be done sequentially.
  Additional processors sit idle while the sequential work is performed.
Thus, it is important to keep in mind that an n-fold increase in processing power does not necessarily result in an n-fold increase in throughput.
Notes: 2

## Slide 3: 9.4 Parallel and Multiprocessor Architectures (3 of 21)
Superscalar architectures include multiple execution units such as specialized integer and floating-point adders and multipliers.
A critical component of this architecture is the instruction fetch unit, which can simultaneously retrieve several instructions from memory.
A decoding unit determines which of these instructions can be executed in parallel and combines them accordingly.
This architecture also requires compilers that make optimum use of the hardware.
Notes: 3

## Slide 4: 9.4 Parallel and Multiprocessor Architectures (5 of 21)
Vector computers are processors that operate on entire vectors or matrices at once.
  These systems are often called supercomputers.
Vector computers are highly pipelined so that arithmetic instructions can be overlapped.
Vector processors can be categorized according to how operands are accessed.
  Register-register vector processors require all operands to be in registers.
  Memory-memory vector processors allow operands to be sent from memory directly to the arithmetic units.
Notes: 4

## Slide 5: 9.4 Parallel and Multiprocessor Architectures (7 of 21)
MIMD systems can communicate through shared memory or through an interconnection network.
Interconnection networks are often classified according to their topology, routing strategy, and switching technique.
Of these, the topology is a major determining factor in the overhead cost of message passing.
Message passing takes time owing to network latency and incurs overhead in the processors.
Notes: 5

## Slide 6: 9.4 Parallel and Multiprocessor Architectures (9 of 21)
Completely Connected
Star
Linear and Ring
Mesh and Mesh Ring
Tree
Four-Dimensional Hypercube
A Bus-Based Network
Notes: 6

## Slide 7: 9.4 Parallel and Multiprocessor Architectures (13 of 21)
Tightly-coupled multiprocessor systems use the same memory. They are also referred to as shared memory multiprocessors.
The processors do not necessarily have to share the same block of physical memory.
Each processor can have its own memory, but it must share it with the other processors.
Configurations such as these are called distributed shared memory multiprocessors.
Notes: 7

## Slide 8: 9.4 Parallel and Multiprocessor Architectures (19 of 21)
Distributed computing is another form of multiprocessing. However, the term distributed computing means different things to different people.
In a sense, all multiprocessor systems are distributed systems because the processing load is distributed among processors that work collaboratively.
The common understanding is that a distributed system consists of very loosely-coupled processing units.
Notes: 8

## Slide 9: 9.4 Parallel and Multiprocessor Architectures (21 of 21)
Cloud computing is distributed computing to the extreme.
It provides services over the Internet through a collection of loosely-coupled systems.
In theory, the service consumer has no awareness of the hardware, or even its location.
  Your services and data may even be located on the same physical system as that of your business competitor.
  The hardware might even be located in another country.
Security concerns are a major inhibiting factor for cloud computing.
Notes: 9

## Slide 10: 9.5 Alternative Parallel Processing Approaches (1 of 15)
Some people argue that real breakthroughs in computational power—breakthroughs that will enable us to solve today’s intractable problems— will occur only by abandoning the von Neumann model.
Numerous efforts are now underway to devise systems that could change the way that we think about computers and computation.
Following, we will look at some examples
Notes: 10

## Slide 11: 9.5 Alternative Parallel Processing Approaches (2 of 15)
Von Neumann machines exhibit sequential control flow: A linear stream of instructions is fetched from memory, and they act upon data.
Program flow changes under the direction of branching instructions.
In dataflow computing, program control is directly controlled by data dependencies.
There is no program counter or shared storage.
Data flows continuously and is available to multiple instructions simultaneously.
Notes: 11

## Slide 12: 9.5 Alternative Parallel Processing Approaches (3 of 15)
A data flow graph represents the computation flow in a dataflow computer.
Its nodes contain the instructions and its arcs indicate the data dependencies.
Notes: 12

## Slide 13: 9.5 Alternative Parallel Processing Approaches (4 of 15)
When a node has all of the data tokens it needs, it fires, performing the required operation.
The result is placed on an output arc.
Notes: 13

## Slide 14: 9.5 Alternative Parallel Processing Approaches (8 of 15)
Neural network computers consist of a large number of simple processing elements that individually solve a small piece of a much larger problem.
They are particularly useful in dynamic situations that are an accumulation of previous behavior, and where an exact algorithmic solution cannot be formulated.
Like their biological analogues, neural networks can deal with imprecise, probabilistic information, and allow for adaptive interactions.
Notes: 14

## Slide 15: 9.5 Alternative Parallel Processing Approaches (9 of 15)
Neural network processing elements (PEs) multiply a set of input values by an adaptable set of weights to yield a single output value.
The computation carried out by each PE is simplistic—almost trivial—when compared to a traditional microprocessor. Their power lies in their massively parallel architecture and their ability to adapt to the dynamics of the problem space.
Neural networks learn from their environments. A built-in learning algorithm directs this process.
Notes: 15

## Slide 16: 9.5 Alternative Parallel Processing Approaches (10 of 15)
The simplest neural net PE is the perceptron.
Perceptrons are trainable neurons. A perceptron produces a Boolean output based upon the values that it receives from several inputs.
Notes: 16

## Slide 17: 9.5 Alternative Parallel Processing Approaches (11 of 15)
Perceptrons are trainable because the threshold and input weights are modifiable.
In this example, the output Z is true (1) if the net input, w1x1 + w2x2 + . . .+ wnxn is greater than the threshold T.
Notes: 17

## Slide 18: 9.5 Alternative Parallel Processing Approaches (12 of 15)
Perceptrons are trained by use of supervised learning.
Supervised learning assumes prior knowledge of correct results, which are fed to the neural net during the training phase. If the output is incorrect, the network modifies the input weights to produce correct results.
Notes: 18

## Slide 19: 9.6 Quantum Computing (1 of 8)
Computers, as we know them are binary, transistor-based systems.
But transistor-based systems strain to keep up with our computational demands.
We increase the number of transistors for more power, and each transistor smaller to fit on the die.
  Transistors are becoming so small that it is hard for them to hold electrons in the way in which we're accustomed to.
Thus, alternatives to transistor-based systems are an active area or research.
Notes: 19

## Slide 20: 9.6 Quantum Computing (2 of 8)
Computers are now being built based on:
  Optics (photonic computing)
  Biological neurons
  DNA
One of the most intriguing is quantum computers.
Quantum computing uses quantum bits (qubits) that can be in multiple states at once.
The “state” of a qubit is determined by the spin of an electron.
A thorough discussion of “spin” is under the domain of quantum physics.
Notes: 20

## Slide 21: 9.6 Quantum Computing (3 of 8)
A qubit can be in multiple states at the same time.
  This is called superpositioning.
A 3-bit register can simultaneously hold the values 0 through 7.
  8 operations can be performed at the same time.
This phenomenon is called quantum parallelism.
  A system with 600 qbits can superposition 2600 states.
Notes: 21

## Slide 22: 9.6 Quantum Computing (4 of 8)
D-Wave Computers is the first quantum computer manufacturer.
D-Wave computers having 512 qbits were purchased separately by University of Southern California and Google for research purposes.
Quantum computers may be applied in the areas of cryptography, true random-number generation, and in the solution of other intractable problems.
Notes: 22

## Slide 23: 9.6 Quantum Computing (5 of 8)
Making effective use of quantum computers requires rethinking our approach to problems and the development of new algorithms.
  To break a cypher, the quantum machine simulates every possible state of the problem set (i.e., every possible key for a cipher) and it “collapses” on the correct solution.
Examples include Schor’s algorithm for factoring products of prime numbers.
Many others remain to be discovered.
Notes: 23

## Slide 24: 9.6 Quantum Computing (6 of 8)
These systems are not constrained by a fetch-decode-execute cycle; however, quantum architectures have yet to settle on a definitive paradigm analogous to von Neumann systems.
Rose’s Law states that the number of qubits that can be assembled to successfully perform computations will double every 12 months; this has been precisely the case for the past 9 years.
  This “law” is named after Geordie Rose, D-Wave’s founder and chief technology officer.
Notes: 24

## Slide 25: 9.6 Quantum Computing (7 of 8)
One of the largest obstacles to the progress of quantum computation is the tendency for qubits to decay into a state of decoherence.
  Decoherence causes uncorrectable errors.
Advanced error-correction algorithms have been applied to this problem and show promise.
Much research remains to be done, however.
Notes: 25

## Slide 26: 9.6 Quantum Computing (8 of 8)
The realization of quantum computing has raised questions about technological singularity.
  Technological singularity is the theoretical point when human technology has fundamentally and irreversibly altered human development.
  This is the point when civilization changes to an extent that its technology is incomprehensible to previous generations.
Are we there, now?
Notes: 26

## Slide 27: Conclusion (1 of 4)
The common distinctions between RISC and CISC systems include RISC’s short, fixed-length instructions. RISC ISAs are load-store architectures. These things permit RISC systems to be highly pipelined.
Flynn’s Taxonomy provides a way to classify multiprocessor systems based upon the number of processors and data streams. It falls short of being an accurate depiction of today’s systems.
Notes: 27

## Slide 28: Conclusion (2 of 4)
Massively parallel processors have many processors, distributed memory, and computational elements communicate through a network. Symmetric multiprocessors have fewer processors and communicate through shared memory.
Characteristics of superscalar design include superpipelining, and specialized instruction fetch and decoding units.
Notes: 28

## Slide 29: Conclusion (3 of 4)
Very long instruction word (VLIW) architectures differ from superscalar architectures because the compiler, instead of a decoding unit, creates long instructions.
Vector computers are highly-pipelined processors that operate on entire vectors or matrices at once.
MIMD systems communicate through networks that can be blocking or nonblocking. The network topology often determines throughput.
Notes: 29

## Slide 30: Conclusion (4 of 4)
Multiprocessor memory can be distributed or exist in a single unit. Distributed memory brings to rise problems with cache coherency that are addressed using cache coherency protocols.
New architectures are being devised to solve intractable problems. These new architectures include dataflow computers, neural networks, systolic arrays, and quantum computers.
Notes: 30